## Slide 1: GPS Equipment for Agricultural Statistics Surveys: Lessons Learned From Fieldwork in Uganda - 2003
Presentation at the Third International Conference on
Agricultural Statistics MEXSAI-ICAS-III
Cancun, Mexico;
2nd to 4th November 2004
Authors:
E. S. K. Muwanga-Zake, J. Magezi-Apuuli, E. Menyha and P. Schøning

## Slide 2: Objective
To discuss the results from a pilot census of Agriculture in Uganda which indicates that there is potential to use relatively cheap Global Positioning System (GPS) equipment for measuring of area and for geo-referencing of holdings in the context of agricultural statistics.

## Slide 3: Presentation covers:
1. Introduction
2. Areas in the Context of Agricultural Statistics
3. Testing of GPS equipment during the Pilot Census of Agriculture, 2003
3.1 Experimental Design
3.2 Comparison of Results of Area Measurements
3.3 Comparison of Results of Time Taken
3.4 Comparison of Costs of the Instruments
3.5 Lessons Learnt
4. Conclusions
5. Issues and Further Work

## Slide 4: Introduction
In Uganda no complete set of cadastral and/or land registers from which to get area information
Food and Agricultural Statistics in general and area statistics, in particular, very poor
During the Pilot Census of Agriculture (PCA) in Uganda, in 2003 it was decided to experiment with different methods and equipment for area, yield estimation, production estimation, compilation of conversion factors, etc.

## Slide 5: Areas in the Context of Agricultural Statistics
Land is one of the most important factors of production
Pattern of land use varies by season, region, etc.
Area Measurement Used for:
Determination of structural changes of agric. Holdings; and;
Estimation of Agricultural Production by
AREA x YIELD

## Slide 6: Comparative studies of methods and tools used for area measurement conducted under the PCA 2003
Four Methods and tools tested were:
  Holder’s/respondent’s Eye-estimate
  Enumerator’s eye-estimates
  Tape and Compass (traversing)
  Global Positioning Systems (GPS) Equipment
Must ensure that the different Methods and tools are INDEPENDENT

## Slide 7: Storing the track-log as vector data i.e. “cadastral mapping”
Filling in questionnaires for area&coordinates
i.e. traditional statistical approach
Possible uses of the GPS Equipment Data

## Slide 8: Technical Specification (GPS) Garmin Handheld GPS 12 / GPS 12XL
Build-in program for area calculation
Satellite tracking <=12
Accuracy <=15 m
Waypoint capacity <=500
Acquisition time 45 sec.
Power source 4 x AA
Battery life 24 hours*
Operating temperature -15OC to +70OC
High contrast display
Features external antenna (GPS 12XL)
Dimensions 2” x 6.15” x 1.23”
Price GPS12: USD 149.50
Price GPS12XL: USD 229.00
* Battery life less than 12h as batteries are
changed when half of power is used.

## Slide 9: Experimental Design (PCA) A trade-off between cost, enumerator’s capacity and scientific design
Holding group I
-Holder’s area eye-estimate
-Measure by tape&compass -Measure by GPS
N = 900 holdings distributed on 60 EAs and 10 Districts
3 strata of 5 holdings in each EA
Different area & crop measurement/estim-ation techniques applied to each stratum
Holding group II + III
-Enumerator’s area
eye-estimate
-Measure by GPS Equip.

## Slide 10: Areas Measured (PCA)
Plot 1
Homestead
Plot 2
Beans
Plot 1
Maize&beans
Plot 3
Coffee
Holding, Parcels and Plots
Parcel 2
Parcel 1
The total area of the holding
Area of each parcel
Area of each crop-plot

## Slide 11: Measuring area with GPS A fast and cost efficient method?
Fix the starting point
Walk the perimeter of the area (plot or parcel)
Calculate area either by:
  (A) Storing of the track-log and calculate the area on a PC
  (B) Calculate the area directly with the GPS tool and fill in the results on a form

## Slide 13: Results from comparative studies (PCA) Results from traversing (tape&compass) compared with results from use of GPS – measuring area at parcel level

## Slide 14: Results from comparative studies (PCA) cont. Measuring area at parcel level
The difference between the two means is highly insignificant and therefore the results obtained by the GPS tool are statistically not different from those obtained by traversing using tape & compass.

## Slide 15: Results from comparative studies (PCA) cont. Minutes used to measure area per holding
191 observations of time used where areas are both measured by traversing (tape & compass) and by GPS
On average GPS measure requires 28.5 percent of the time required for traversing the same areas

## Slide 16: Comparative Costs
GPS Equipment
Fairly expensive
GPS model used cost about US$150 per Unit
3 Enumerators shared 2 GPS equipment
Used 4 expensive high quality AA batteries @US$1.25 per pair
Tape and Compass
Tape about US$25
Compass about US$100
Need programmable calculator (fairly expensive)
Enumerator needs assistance for tape

## Slide 17: Additional test I: Variation between tools using several GPS tools
7 x GPS tools tested in 3 districts
Very little variance both between tools and for each tool when repeated observation in Wakiso
More variance both between tools and for each tool when repeated observation in Kabarole I-II (more difficult terrain?)
Too few observations to draw robust conclusions
Measure of plot areas. m2

## Slide 18: Additional test II: Variation over time using the same GPS tool
1 x GPS tool tested 22 times on the same area
Reasonable variation +/- around the true value
Mean of observations deviates 1.9 percent from the true value
Median of observations deviates 0.1 percent from the true value
The range is wide
Plot area (m2) measured by GPS (January 2003)
Lower Bound
462.22
Median
482.50
Variance
722.89
Std. Deviation
26.89
Minimum
407.00
Maximum
510.00
Statistics
Std. Error
Number of observations
22
Mean
474.14
5.73
95% Confidence Interval for Mean
Upper Bound
486.06
Range
103.00
Plot area (m2) measured by GPS (January 2003)
Lower Bound
462.22
Median
482.50
Variance
722.89
Std. Deviation
26.89
Minimum
407.00
Maximum
510.00
Statistics
Std. Error
Number of observations
22
Mean
474.14
5.73
95% Confidence Interval for Mean
Upper Bound
486.06
Range
103.00
Plot area (m2) measured by GPS (January 2003)
Lower Bound
462.22
Median
482.50
Variance
722.89
Std. Deviation
26.89
Minimum
407.00
Maximum
510.00
Statistics
Std. Error
Number of observations
22
Mean
474.14
5.73
95% Confidence Interval for Mean
Upper Bound
486.06
Range
103.00
Plot area measurement.
Testing of variation of 1x GPS
True value 483 m2

## Slide 19: Lessons learned using GPS
Cost efficient tool with acceptable accuracy
Easy to use even for trained non-experts
The instrument gives “high-tech status” to the Enumerator i.e. built-in motivation for use
Can also be used to geo-reference holdings (x/y coordinates)
Set-up facilities are vulnerable for un-prescribed changes
Battery consumption is high
Steep slopes give inaccurate results (projection problems +)
Dense tree canopy gives inaccuracy (consider to use extended antenna)

## Slide 20: Conclusions
Area measurements by the GPS equipment and those by the compass and tape are very close – no statistically significant difference for parcel areas
Farmers overestimated areas for both parcels and plots compared to GPS and traversing technique.
GPS equipment is much faster and costs are fairly comparable to those of traversing, so there is a potential for the GPS equipment for agricultural area measurements
There is need for cheaper GPS equipment and reduction of running costs or at least more efficient use
There is also need for more thorough training of field staff.
More study is required on the variability and consistency of the equipment
Special studies concerning effects of steep slopes and under tree and cloud cover should also be conducted

## Slide 21: Issues and Further Work
Can an international effort be made to develop a GPS version specifically for area measurement?
Are there other versions of the GPS equipment that can be more cost-efficient?
Could improve efficiency in use GPS tools e.g.switch off when not in use; more enumerators to share single equipment.
Could use re-chargeable batteries as more cost-efficient option.

## Slide 22
GRACIAS A TODOS / Thanks you all
The End